# Text boxes

LIMITED

LIABILITY COMPANY

LASERTAG

SPECIFICATION

ALICE VEST

Smolensk

1. Description

The ALICE VEST is a fabric vest with 8 hit sensors and 2 control units. Designed to play laser tag and fire tag.

2. Contents of delivery:

- ALICE VEST with hit sensors	- 1 pc.

- Specification	- 1 pc.

3. Main technical description

| Voltage (volt). | 7.4 |
| --- | --- |
| Battery capacity, Ah | 2.2 |
| Weight, kg | 0.956 |
| Battery type | Li+ |
| Number of hit sensors | 8 |

4. Maintenance

All parts of the set must be treated with care if you want the equipment to function properly. There shouldn't be any moisture inside the frame. Don't hit the device.

5. User's manual

The "vest to gun" connection algorithm

- Turn on the gun.

- Turn on the vest.

- Wait for their connection (the device will make a sound. There will also be a light and vibro indication as well).

- Activate the kit device using a remote control or a first aid kit.

The "Headband (helmet) to Vest to Gun" connection algorithm.

- Turn on the gun.

- Turn on the vest.

- Turn on the headband (helmet).

- Wait for connection.

- Activate the game set with the help of a remote control or a first aid kit.

The "Vest to Gun to Gun" connection algorithm.

- Turn on the first gun.

- Turn on the vest.

- Wait for their connection.

- Turn on the second rifle.

- Wait for some time. It will connect to the vest (the vibration will stop after a short signal).

- Activate the game set with a remote control or a first aid kit.

Game set connection algorithm

"Headband (helmet) to Vest to Gun to Gun"

- Turn on the first gun.

- Turn on the vest.

- Turn on the headband (helmet).

- Wait for their connection.

- Turn on the second rifle.

- Wait for its connection to the game set.

- Activate the game set using a remote control or a first aid kit.

The vest can be used in with or without a headband. Based on the 8-th generation of electronics.

2

3

6. Guarantee obligations

The manufacturer guarantees the reliability of the operation of an individual LASERWAR set if the consumer has complied with the conditions of use. Technical support is provided within 12 months of the sale date. The manufacturer undertakes to replace or repair an individual set of equipment free of charge, if the customer has complied with the rules for the device transportation, storage, operation and delivery of defective equipment to Smolensk City.

7. Contact information

| Official website: www.laserwar.ru E-mail: info@laserwar.ru support@laserwar.ru Skype: info-laserwar.ru support laserwar.ru |  |
| --- | --- |

______________________________________

Equipment Maintenance Rules

1. Weather conditions. At the course of manufacture, we make different tests to see how well the equipment works under different weather conditions. Despite this, we strongly recommend that the equipment shouldn’t be used in the rain and at temperatures below -20 ° C.

What should I know when using the equipment in poor weather conditions?

The most important thing is to avoid getting moisture inside the device. If this happened, turn off the device, dry the equipment at room temperature for at least two hours.

2. Power source. The ALICE VEST has 7.4 v. lithium batteries.

To recharge the device use only Li+ chargers.

Charge the device under supervision for three hours.

It is necessary to store the equipment in a well-ventilated room at temperature from + 18°C to + 30°C and relative humidity of 45-65%.

The warranty is 14 days for batteries, speakers, and IR modules. These components are expendable materials.

PLEASE NOTE! In the case of improper operation of the accumulator (charging by an unrelated type of a charger), the warranty doesn't cover the battery!

5

4

Dear Customer!

Our company welcomes and thanks you for the decision to buy our products, and is confident that the purchased device will bring you a long-term pleasure. The warranty certificate establishes the guarantee of the product in the amount provided for by the Law on consumer protection of the Russian Federation.

This warranty certificate is valid for 12 months from the purchase date of the product, and is subject to the guarantee terms.

Warranty Terms:

1. The guarantee is effective upon presentation of this coupon, which shall contain the serial number of the product and the date of its purchase, confirmed by the service centre.

2. These guarantee obligations apply to products acquired only from the official LASERTAG representative or the official dealer.

3. The present guarantee is invalid if the product deficiencies have occurred in the following cases:

- failure to comply with Operating instructions;

- mechanical damage;

- penetration of extraneous items, liquids, etc.;

- animal activities;

- unauthorized access to the parts of the game set by non-authorized persons;

- use of the product for purposes for which it hasn't been made;

- Acts of elements (natural disaster, fire, accidents, etc.);

- the game set malfunction in case of faulty power network and/or poor care of the product.

4. If the warranty certificate is lost, no duplicate is issued.

Information on the repairs performed during the maintenance period (completed by the Service centre performing the warranty repair works).

| Date: __________________ Completed work: _____________________________________________________________________ Service centre stamp | Date: __________________ Completed work: _____________________________________________________________________ Service centre stamp |
| --- | --- |
| Date: __________________ Completed work: _____________________________________________________________________ Service centre stamp | Date: __________________ Completed work: _____________________________________________________________________ Service centre stamp |
| Date: __________________ Completed work: _____________________________________________________________________ Service centre stamp | Date: __________________ Completed work: _____________________________________________________________________ Service centre stamp |

7

6